## Slide 1: General Considerations: Units in RF Design
This relationship between Power and Voltage only holds when the input and output impedance are equal
An amplifier senses a sinusoidal signal and delivers a power of 0 dBm to a load resistance of 50 Ω. Determine the peak-to-peak voltage swing across the load.
Solution:
where RL= 50 Ω thus,

## Slide 2: Example of Units in RF
Solution:
Output voltage of the amplifier is of interest in this example
A GSM receiver senses a narrowband (modulated) signal having a level of -100 dBm. If the front-end amplifier provides a voltage gain of 15 dB, calculate the peak-to-peak voltage swing at the output of the amplifier.
Since the amplifier output voltage swing is of interest, we first convert the received signal level to voltage. From the previous example, we note that -100 dBm is 100 dB below 632 mVpp. Also, 100 dB for voltage quantities is equivalent to 105. Thus, -100 dBm is equivalent to 6.32 μVpp. This input level is amplified by 15 dB (≈ 5.62), resulting in an output swing of 35.5 μVpp.

## Slide 3: dBm Used at Interfaces Without Power Transfer
dBm can be used at interfaces that do not necessarily entail power transfer
We mentally attach an ideal voltage buffer to node X and drive a 50-Ω load. We then say that the signal at node X has a level of 0 dBm, tacitly meaning that if this signal were applied to a 50-Ω load, then it would deliver 1 mW.

## Slide 4: General Considerations: Time Variance
A system is linear if its output can be expressed as a linear combination (superposition) of responses to individual inputs.
A system is time-invariant if a time shift in its input results in the same time shift in its output.
If y(t) = f [x(t)]
then y(t-τ) = f [x(t-τ)]

## Slide 5: Nonlinearity: Memoryless and Static System
In this idealized case, the circuit displays only second-order nonlinearity
linear
nonlinear
The input/output characteristic of a memoryless nonlinear system can be approximated with a polynomial

## Slide 6: Effects of Nonlinearity: Harmonic Distortion
Even-order harmonics result from αj with even j
nth harmonic grows in proportion to An
DC
Fundamental
Second
Harmonic
Third
Harmonic
The output of a “dynamic” system depends on the past values of its input/output
Linear Time-invariant Linear Time-variant

## Slide 7: Example of Harmonic Distortion in Mixer
Solution:
An analog multiplier “mixes” its two inputs below, ideally producing y(t) = kx1(t)x2(t), where k is a constant. Assume x1(t) = A1 cos ω1t and x2(t) = A2 cos ω2t.
If the mixer is ideal, determine the output frequency components.
(b) If the input port sensing x2(t) suffers from third-order nonlinearity, determine the output frequency components.
(a)
(b)

## Slide 8
Example of Harmonics on GSM Signal
Solution:
The transmitter in a 900-MHz GSM cellphone delivers 1 W of power to the antenna. Explain the effect of the harmonics of this signal.
The second harmonic falls within another GSM cellphone band around 1800 MHz and must be sufficiently small to negligibly impact the other users in that band. The third, fourth, and fifth harmonics do not coincide with any popular bands but must still remain below a certain level imposed by regulatory organizations in each country. The sixth harmonic falls in the 5-GHz band used in wireless local area networks (WLANs), e.g., in laptops. Figure below summarizes these results.

## Slide 9: Gain Compression: 1-dB Compression Point
Output falls below its ideal value by 1 dB at the 1-dB compression point
Peak value instead of peak-to-peak value

## Slide 10: Gain Compression: Desensitization
Desensitization: the receiver gain is reduced by the large excursions produced by the interferer even though the desired signal itself is small.
For A1 << A2

## Slide 11: Example of Gain Compression
Solution:
A 900-MHz GSM transmitter delivers a power of 1 W to the antenna. By how much must the second harmonic of the signal be suppressed (filtered) so that it does not desensitize a 1.8-GHz receiver having P1dB = -25 dBm? Assume the receiver is 1 m away and the 1.8-GHz signal is attenuated by 10 dB as it propagates across this distance.
The output power at 900 MHz is equal to +30 dBm. With an attenuation of 10 dB, the second harmonic must not exceed -15 dBm at the transmitter antenna so that it is below P1dB of the receiver. Thus, the second harmonic must remain at least 45 dB below the fundamental at the TX output. In practice, this interference must be another several dB lower to ensure the RX does not compress.

## Slide 12: Effects of Nonlinearity: Intermodulation— Recall Previous Discussion
Single Signal
Signal + one large interferer
Signal + two large interferers
Harmonic distortion
Desensitization
Intermodulation
So far we have considered the case of:

## Slide 13: Effects of Nonlinearity: Intermodulation
assume
Thus
Intermodulation products:
Fundamental components:

## Slide 14: Intermodulation Product Falling on Desired Channel
desired
Interferer
A received small desired signal along with two large interferers
Intermodulation product falls onto the desired channel, corrupts signal.

## Slide 15: Example of Intermodulation
Solution:
Suppose four Bluetooth users operate in a room as shown in figure below. User 4 is in the receive mode and attempts to sense a weak signal transmitted by User 1 at 2.410 GHz. At the same time, Users 2 and 3 transmit at 2.420 GHz and 2.430 GHz, respectively. Explain what happens.
Since the frequencies transmitted by Users 1, 2, and 3 happen to be equally spaced, the intermodulation in the LNA of RX4 corrupts the desired signal at 2.410 GHz.

## Slide 16: Intermodulation: Tones and Modulated Interferers
In intermodulation Analyses:
(a) approximate the interferers with tones
(b) calculate the level of intermodulation products at the output
(c) mentally convert the intermodulation tones back to modulated components
so as to see the corruption.

## Slide 17: Example of Gain Compression and Intermodulation
Solution:
A Bluetooth receiver employs a low-noise amplifier having a gain of 10 and an input impedance of 50 Ω. The LNA senses a desired signal level of -80 dBm at 2.410 GHz and two interferers of equal levels at 2.420 GHz and 2.430 GHz. For simplicity, assume the LNA drives a 50-Ω load.
(a) Determine the value of α3 that yields a P1dB of -30 dBm.
(b) If each interferer is 10 dB below P1dB, determine the corruption experienced by the desired signal at the LNA output.
(a) From previous equation, α3 = 14.500 V-2
(b) Each interferer has a level of -40 dBm (= 6.32 m Vpp), we determine the amplitude of the IM product at 2.410 GHz as:

## Slide 18
Intermodulation: Third Intercept Point
IP3 is not a directly measureable quantity, but a point obtained by extrapolation

## Slide 19: Example of Third Intercept Point
Solution:
A low-noise amplifier senses a -80-dBm signal at 2.410 GHz and two -20-dBm interferers at 2.420 GHz and 2.430 GHz. What IIP3 is required if the IM products must remain 20 dB below the signal? For simplicity, assume 50-Ω interfaces at the input and output.
At the LNA output:
Thus

## Slide 20: Effects of Nonlinearity: Cascaded Nonlinear Stages
Considering only the first- and third-order terms, we have:
Thus,

## Slide 21: Cascaded Nonlinear Stages: Intuitive results
To “refer” the IP3 of the second stage to the input of the cascade, we must divide it by α1. Thus, the higher the gain of the first stage, the more nonlinearity is contributed by the second stage.

## Slide 22: IM Spectra in a Cascade (Ⅰ)
Let us assume x(t) =Acos ω1t + Acos ω2t and identify the IM products in a cascade:

## Slide 23: IM Spectra in a Cascade (Ⅱ)
Adding the amplitudes of the IM products, we have
Add in phase as worst-case scenario
Heavily attenuated in narrow-band circuits
Thus, if each stage in a cascade has a gain greater than unity, the nonlinearity of the latter stages becomes increasingly more critical because the IP3 of each stage is equivalently scaled down by the total gain preceding that stage.
For more stages:

## Slide 24: Example of Cascaded Nonlinear Stages
Solution:
A low-noise amplifier having an input IP3 of -10 dBm and a gain of 20 dB is followed by a mixer with an input IP3 of +4 dBm. Which stage limits the IP3 of the cascade more?
With α1 = 20 dB, we note that
Since the scaled IP3 of the second stage is lower than the IP3 of the first stage, we say the second stage limits the overall IP3 more.

## Slide 25: Noise: Noise as a Random Process
Higher temperature
The average current remains equal to VB/R but the instantaneous current displays random values
T must be long enough to accommodate several cycles of the lowest frequency.

## Slide 26: Measurement of Noise Spectrum
To measure signal’s frequency content at 10 kHz, we need to filter out the remainder of the spectrum and measure the average power of the 10-kHz component.

## Slide 27: Noise Spectrum: Power Spectral Density (PSD)
One-Sided
Two-Sided
Total area under Sx(f) represents the average power carried by x(t)

## Slide 28
Example of Noise Spectrum
A resistor of value R1 generates a noise voltage whose one-sided PSD is given by
where k = 1.38 × 10-23 J/K denotes the Boltzmann constant and T the absolute temperature. Such a flat PSD is called “white” because, like white light, it contains all frequencies with equal power levels.
(a) What is the total average power carried by the noise voltage?
(b) What is the dimension of Sv(f)?
(c) Calculate the noise voltage for a 50-Ω resistor in 1 Hz at room temperature.
(a) The area under Sv(f) appears to be infinite, an implausible result because the resistor noise arises from the finite ambient heat. In reality, Sv(f) begins to fall at f > 1 THz, exhibiting a finite total energy, i.e., thermal noise is not quite white.
(b) The dimension of Sv(f) is voltage squared per unit bandwidth (V2/Hz)
(c) For a 50-Ω resistor at T = 300 K

## Slide 29: Effect of Transfer Function on Noise/ Device Noise
Define PSD to allow many of the frequency-domain operations used with deterministic signals to be applied to random signals as well.
Noise can be modeled by a series voltage source or a parallel current source
Polarity of the sources is unimportant but must be kept same throughout the calculations

## Slide 30
Example of Device Noise
Sketch the PSD of the noise voltage measured across the parallel RLC tank depicted in figure below.
Modeling the noise of R1 by a current source and noting that the transfer function Vn/In1 is, in fact, equal to the impedance of the tank, ZT , we write
At f0, L1 and C1 resonate, reducing the circuit to only R1. Thus, the output noise at f0
is simply equal to 4kTR1. At lower or higher frequencies, the impedance of the tank falls and so does the output noise.

## Slide 31: Can We Extract Energy from Resistor?
Available noise power
Suppose R2 is held at T = 0 K (No noise)
This quantity reaches a maximum if R2 = R1 :
PR2,max = kT

## Slide 32: A Theorem about Lossy Circuit
If the real part of the impedance seen between two terminals of a passive (reciprocal) network is equal to Re{Zout}, then the PSD of the thermal noise seen between these terminals is given by 4kTRe{Zout}
An example of transmitting antenna, with radiation resistance Rrad

## Slide 33: Noise in MOSFETS
Thermal noise of MOS transistors operating in the saturation region is approximated by a current source tied between the source and drain terminals, or can be modeled by a voltage source in series with gate.

## Slide 34: Gate-induced Noise Current
At very high frequencies thermal noise current flowing through the channel couples to the gate capacitively

## Slide 35: Flicker Noise and An Example
Can the flicker noise be modeled by a current source?
Yes, a MOSFET having a small-signal voltage source of magnitude V1 in series with its gate is equivalent to a device with a current source of value gmV1 tied between drain and source. Thus,
Notes: K=10^-28 for PMOS, 50 times larger for NMOS
1. Flicker noise is more of a problem in FETs than BJT
2. Worse in NMOS than PMOS
3. Worse for smaller devices
4. 1/f noise adds to the thermal drain current noise

## Slide 36: Noise in Bipolar Transistors
In low-noise circuits, the base resistance thermal noise and the collector current shot noise become dominant.
Bipolar transistors contain physical resistances in their base, emitter, and collector regions, all of which generate thermal noise. Moreover, they also suffer from “shot noise” associated with the transport of carriers across the base-emitter junction.

## Slide 37: Representation of Noise in Circuits Input-Referred Noise
Voltage source: short the input port of models A and B and equate their output noise voltage
Current source: leave the input ports open and equate the output noise voltage

## Slide 38
Example of Input-Referred Noise
noise voltage
noise current
Solution:
Calculate the input-referred noise of the common-gate stage depicted in figure below (left). Assume I1 is ideal and neglect the noise of R1.

## Slide 39: Noise Figure
Depends on not only the noise of the circuit under consideration but the SNR provided by the preceding stage
If the input signal contains no noise, NF=∞
Noise Factor
Noise Figure
Notes: Noise Factor = F = total noise power at the output / output noise due to input noise
Noise factor measures how much the system degrades the SNR of the signal
Noise Figure is the Noise factor expressed in dB.

## Slide 40: Calculation of Noise Figure
NF must be specified with respect to a source impedance-typically 50 Ω
Reduce the right hand side to a simpler form:

## Slide 41: Calculation of NF: Summary
Divide total output noise by the gain from Vin to Vout and normalize the result to the noise of Rs
Calculation of NF
Calculate the output noise due to the amplifier, divide it by the gain, normalize it to 4kTRs and add 1 to the result

## Slide 42
Example of Noise Figure Calculation
Solution:
Compute the noise figure of a shunt resistor RP with respect to a source impedance RS
Setting Vin to zero:

## Slide 43
Another Example of Noise Figure Calculation
Solution:
Determine the noise figure of the common-source stage shown in below (left) with respect to a source impedance RS. Neglect the capacitances and flicker noise of M1 and assume I1 is ideal.

## Slide 44
Noise Figure of Cascaded Stages
Called “Friis’ equation”, stage increases, implying that the first few stages in a cascade are the most critical. this result suggests that the noise contributed by each stage decreases as the total gain preceding that

## Slide 45: Noise Figure of Lossy Circuits
The power loss is calculated as:

## Slide 46
Example of Noise Figure of Lossy Circuits
Solution:
The receiver shown below incorporates a front-end band-pass filter (BPF) to suppress some of the interferers that may desensitize the LNA. If the filter has a loss of L and the LNA a noise figure of NFLNA, calculate the overall noise figure. For example, if L = 1.5 dB and NFLNA = 2 dB
Denoting the noise figure of the filter by NFfilt,
we write Friis’ equation as
where NFLNA is calculated with respect to the output resistance of the filter. For example, if L = 1.5 dB and NFLNA = 2 dB, then NFtot = 3.5 dB.