## Slide 1: Lesson 10. Operational Amplifier

## Slide 2
Introduction
Inverting & Non-inverting Amplifier
Linear Op-Amp Applications
Bias Current and Bandwidth Limitations
Explain basic concepts and definitions of an operational amplifier.
Explain fundamental circuits and applications using the operational amplifier.
Understand practical limitations of the operational amplifier.

## Slide 3: 1. Introduction
1.1. Ideal Op-Amp
1.2. Practical Op-Amp
1.3. Block Diagram of an Op-Amp
1.4. Signal Modes
1.5. Parameters

## Slide 4: 1. Introduction
1.1. Ideal Op-Amp
Operational amplifiers (op-amps) are very high gain dc coupled amplifiers with differential inputs.
One of the inputs is called the inverting input (-); the other is called the noninverting input. Usually there is a single output.
Most op-amps operate from plus and minus supply voltages, which may or may not be shown on the schematic symbol.

## Slide 5: 1. Introduction
1.1. Ideal Op-Amp
Simplify analysis of op-amp circuits.
Ideally, op-amps have infinite voltage gain, infinite bandwidth, infinite input impedance and zero output impedance.
Basic operating principles
Negligible current into its inputs
Difference between the inputs 0.
Limited by what its power supply
∞
∞

## Slide 6: 1. Introduction
1.2. Practical Op-Amp
Practical op-amps have characteristics that often can be treated as ideal for certain situations but can never actually attain ideal characteristics. In addition to finite gain, bandwidth, and input impedance, they have other limitations.

## Slide 7: 1. Introduction
1.2. Practical Op-Amp
Op Amp transfer characteristic curve
saturation
active region
Voutput = b (V+ – V–)
Open Loop Configuration is not useful.

## Slide 8: 1. Introduction
1.2. Practical Op-Amp
Open Loop Configuration
+
–
V–
V+
Voutput
Voutput = A (V+ – V–)
Gain A = 106
When input difference is 15 µV, the output is 15 V, the power supply maximum.

## Slide 9: 1. Introduction
1.3. Block Diagram of an Operational Amplifier
Internally, the typical op-amp has a differential input, a voltage amplifier, and a push-pull output. The differential amplifier amplifies the difference in the two inputs.

## Slide 10: 1. Introduction
1.4. Signal Modes
The input signal can be applied to an op-amp in differential-mode or in common-mode.
Differential-mode signals are applied either as
single-ended (one side on ground) or
double-ended (opposite phases on the inputs).
Differential signals

## Slide 11: 1. Introduction
1.4. Signal Modes
The input signal can be applied to an op-amp in differential-mode or in common-mode.
Common-mode signals are applied to both sides with the same phase on both.
Usually, common-mode signals are from unwanted sources, and affect both inputs in the same way.
The result is that they are essentially cancelled at the output.
Common-mode signals

## Slide 12: 1. Introduction
1.4. Signal Modes
Common-Mode Rejection Ratio
The ability of an amplifier to amplify differential signals and reject common-mode signals is called the common-mode rejection ratio (CMRR).
CMRR is defined as
where Aol is the open-loop differential-gain and Acm is the common-mode gain
CMRR can also be expressed in decibels as

## Slide 13: 1. Introduction
1.4. Signal Modes
Common-Mode Rejection Ratio
Example:
  What is CMRR in decibels for a typical 741C op-amp?
  The typical open-loop differential gain for the 741C is 200,000 and the typical common-mode gain is 6.3.
Solution:
(The minimum specified CMRR is 70 dB)
90 dB

## Slide 14: 1. Introduction
1.5. Parameters
ZIN(d) : The differential input impedance is the total resistance between the inputs
ZIN(cm) : The common-mode input impedance is the resistance between each input and ground
Zout: The output impedance is the resistance viewed from the output of the circuit.

## Slide 15: 1. Introduction
1.5. Parameters
The slew rate is the maximum rate of change of the output voltage in response to a step input voltage
Example: Determine the slew rate for the output response to a step input.
Solution:
= 6 V/ms

## Slide 16: 2. Inverting and Noninverting Amplifier
2.1. Negative Feedback
2.2. Noninverting Amplifier
2.3. Inverting Amplifier

## Slide 17: 2. Inverting and Noninverting Amplifier
17
Negative feedback is the process of returning a portion of the output signal to the input with a phase angle that opposes the input signal.
The advantage of negative feedback is that precise values of amplifier gain can be set. In addition, bandwidth and input/output impedances can be controlled.
2.1. Negative Feedback

## Slide 18: 2. Inverting and Noninverting Amplifier
18
A noninverting amplifier is a configuration in which the signal is on the noninverting input and a portion of the output is returned to the inverting input.
2.2. Noninverting Amplifier
Feedback forces Vf to be equal to Vin, hence Vin is across Ri.
The closed-loop gain of the noninverting amplifier is:
Shall we prove it ?

## Slide 19: 2. Inverting and Noninverting Amplifier
19
2.2. Noninverting Amplifier
What happens when “A” is very large?
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 20: 2. Inverting and Noninverting Amplifier
20
2.2. Noninverting Amplifier
Closed-loop gain
Af=vo/vin
Gain
Closed-loop gain: determined by resistor ratio
insensitive to A, temperature
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 21: 2. Inverting and Noninverting Amplifier
21
2.2. Noninverting Amplifier
Example: Determine the gain of the noninverting amplifier shown.
Solution:
= 25.8
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 22: 2. Inverting and Noninverting Amplifier
22
2.2. Noninverting Amplifier
A special case of the inverting amplifier is when Rf =0 and Ri = ∞.
Voltage Follower (unity gain buffer with a gain of 1)
+
–
VN
VP
Voutput
A(VP–VN )=Vo
but Vo = VN
so A(VP–Vo )=Vo
AVP=Vo + AVo
AVP=(1 + A)Vo
But A is huge (106)
A  (1 + A)
VP=Vo
Purpose: A voltage follower buffers a delicate investigation system from a demanding measurement system.
Notes: The input impedance of the voltage follower is very high, producing an excellent circuit for isolating one circuit from another, which avoids "loading" effects.
Op amp draws negligible input current (not disturbing the investigation system) while being able to deliver significant output current (to meet the demands of the measurement system) in such a way that the output voltage is the same as the input voltage.

## Slide 23: 2. Inverting and Noninverting Amplifier
23
2.3. Inverting Amplifier
An inverting amplifier is a configuration in which the noninverting input is grounded and the signal is applied through a resistor to the inverting input.
Feedback forces the inputs to be nearly identical; hence the inverting input is very close to 0 V. The closed-loop gain of the inverting amplifier is
0 V (virtual ground)
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 24: 2. Inverting and Noninverting Amplifier
24
2.3. Inverting Amplifier
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 25: 2. Inverting and Noninverting Amplifier
2.3. Inverting Amplifier
We can adjust the closed-loop gain by changing the ratio of R2 and R1.
We can make it arbitrarily large or small and with the desired accuracy depending on the accuracy of the resistors.
The terminal 1 is a virtual ground since terminal 2 is grounded
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 26: 2. Inverting and Noninverting Amplifier
2.3. Inverting Amplifier
Example: Determine the gain of the inverting amplifier shown.
Solution:
= -24.8
The minus sign indicates inversion.
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 27: 3. Linear Op-Amp Applications
3.1. Summing & Averaging
3.2. Scaling Adder
3.3. Subtracting
3.4 Practical Applications

## Slide 28: 3. Linear Op-Amp Applications
28
3.1. Summing & Averaging
Summing Amplifiers
For node N，
Let
Rf /R = 1/3 => Averaging
Summing
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 29: 3. Linear Op-Amp Applications
3.1. Summing & Averaging
Example: Assume R1 = R2 = R3 = 10 kW and Rf = 3.3 kW?
Solution:
VOUT = -⅓(VIN1 + VIN2 + VIN3)
= -⅓(+5.0 V - 3.5 V + 4.2 V)
= -1.9 V
Example: What is VOUT if the input voltages are +5.0 V, -3.5 V and +4.2 V and all resistors = 10 kW?
Solution:
VOUT = -(VIN1 + VIN2 + VIN3)
= -(+5.0 V - 3.5 V + 4.2 V)
= -5.7 V
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 30: 3. Linear Op-Amp Applications
3.2. Scaling Adder
Scaling Adder (Weighted Summer)
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 31: 3. Linear Op-Amp Applications
3.2. Scaling Adder
Example: Assume you need to sum the inputs from three microphones. The first two microphones require a gain of -2, but the third microphone requires a gain of -3. What are the values of the input Rs (R1 , R2 , R3) if Rf = 10 kΩ?
Solution:
5.0 kW
3.3 kW
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 32: 3. Linear Op-Amp Applications
3.2. Scaling Adder
An application of a scaling adder is the D/A converter circuit shown here. The resistors are inversely proportional to the binary column weights.
Because of the precision required of resistors, the method is useful only for small DACs.
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 33: 3. Linear Op-Amp Applications
3.2. Scaling Adder
0
0 1 0
1
0
0 1
1
0 1 0
0
1.5
2
0 1 0 1
0 1
1 0
0 1
1
1
1 0
0
0
2.5
3
3.5
4
1 0
0 1
1 0 1 0
1 0 1
1
1
1 0
0
1
1 0 1
1
1
1 0
1
1
1
1
4.5
5
5.5
6
6.5
7
7.5
Binary
number
Analog
output
(volts)
0
0
0
0
0
0
0
0 1
.5
MSB
LSB
S1 closed if LSB =1
S2 " if next bit = 1
S3 " if " " = 1
S4 " if MSB = 1
4-Bit D/A
8V
-
+
V0
5K
80K
40K
20K
10K
S1
+ -
S3
S2
S4
-
+
“Weighted-adder D/A converter”
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 34: 3. Linear Op-Amp Applications
3.2. Scaling Adder
Digital Input
0
1
2
3
4
5
6
7
8
0
2
4
6
8
10
12
14
16
Analog Output (V)
1111
1000
0100
0000
0001
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 35: 3. Linear Op-Amp Applications
3.3. Subtracting Amplifier
+
–
V1
Vo
Rf
R1
V2
R2
R3
With inverting and non-inverting amplifier, we can determine the difference between two voltages.
R1 = R2 and Rf = R3, then
Vo = [Rf/R1] (V2 - V1)
R1 = R2 = Rf = R3, then
Vo = (V2 - V1)
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 36: 3. Linear Op-Amp Applications
3.4. Practical Applications
Vo = [Rf/Rin] (Vt - Vs)  T(Vo)
+
–
Vo
Rin
Rin
Rf
Rf
Standard temperature 0 ˚C
Test temperature ?
Vs
Vt
copper
copper
constantan
A Thermocouple
Thermocouples are used in pairs.
The voltage difference is related to the temperature.
A difference amplifier is perfect for this job.

## Slide 37: 3. Linear Op-Amp Applications
37
A Spectrometer
A photodiode can be used as a transducer;
Its resistance changes when light impinges on it.
Resistance is inversely proportional to the power of the impinging light source.
3.4. Practical Applications
+
–
Vsource
Vo
Rref
Rsample
Sample
solution
Reference
solution (blank)
Vo = -(Rref/Rsample) Vsource
Vo = k (Psample/Pref)
Notes: May do Quang pho

## Slide 38: 4. Bias Current and Bandwidth Limitations
4.1. Bias Current Compensation
4.2. Bandwidth Limitations

## Slide 39: 4. Bias Current and Bandwidth Limitations
4.1. Bias Current Compensation
For op-amps with a BJT input stage, bias current can create a small output error voltage.
To compensate for this, a resistor equal to Ri||Rf is added to one of the inputs.
Noninverting amplifier
Inverting amplifier
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 40: 4. Bias Current and Bandwidth Limitations
4.2. Bandwidth Limitations
Many op-amps have a roll off rate determined by a single low-pass RC circuit, giving a constant -20 dB/decade down to unity gain.
Op-amps with this characteristic are called compensated op-amps.
The blue line represents the open-loop frequency characteristic (Bode plot) for the op-amp.
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 41: 4. Bias Current and Bandwidth Limitations
4.2. Bandwidth Limitations
For op-amps with a -20 dB/decade open-loop gain, the closed-loop critical frequency is given by fc(cl) = fc(ol)(1 + BAol(mid))
The closed-loop critical frequency is higher than the open-loop critical frequency by the factor (1 + BAol(mid)). This means that you can achieve a higher BW by accepting less gain.
For a compensated op-amp, Acl f(cl) = Aol fc(ol) = fT
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 42: 4. Bias Current and Bandwidth Limitations
4.2. Bandwidth Limitations
The equation, Acl f(cl) = Aol fc(ol) shows that the product of the gain and bandwidth are constant.
The gain-bandwidth product is also equal to the unity gain frequency.
That is fT = Acl fc(cl), where fT is the unity-gain bandwidth.
Example: The fT for a 741C op amp is 1 MHz. What is the BWcl for the amplifier?
Solution:
38.8 kHz
Notes: Để đánh giá tần số cắt do tụ Cc ảnh hưởng, ta cần biểu diễn hệ số khuếch đại điện áp là tỉ số giữa Vo trên RL và điện áp khuếch đại không tải.
Áp dụng cách thức đã trình bày ở mục 2.2.

## Slide 43: Quiz 1.
Quiz Number | 1 | Quiz Type | OX | Example Select
Question | The ideal op-amp has |  |  | 
Example | Zero input impedance and zero output impedance Zero input impedance and infinite output impedance Infinite input impedance and zero output impedance Infinite input impedance and infinite output impedance |  |  | 
Answer | C |  |  | 
Feedback |  |  |  | 

## Slide 44: Quiz 2.
Quiz Number | 2 | Quiz Type | OX | Example Select
Question | Given a noninverting amplifier with a gain of 10 and a gain-bandwidth product of 1.0 MHz, the expected high critical frequency is |  |  | 
Example | 100 Hz 1.0 kHz 10 kHz 100 kHz |  |  | 
Answer | D |  |  | 
Feedback |  |  |  | 

## Slide 45: Summary
Operational amplifier: A type of amplifier that has very high voltage gain, very high input impedance, very low output impedance and good rejection of common-mode signals.
Differential mode: A mode of op-amp operation in which two opposite-polarity signals voltages are applied to the two inputs (double-ended) or in which a signal is applied to one input and ground to the other input (single-ended).
Common mode: A condition characterized by the presence of the same signal on both inputs
Open-loop voltage gain: The voltage gain of an op-amp without external feedback.
Negative feedback: The process of returning a portion of the output signal to the input of an amplifier such that it is out of phase with the input.
Closed-loop voltage gain: The voltage gain of an op-amp with external feedback.
Gain-bandwidth product: A constant parameter which is always equal to the frequency at which the op-amp’s open-loop gain is unity (1).
Notes: Trang tổng kết bài học
Đề mục 1. Solving….Tree: font size 20 , noi dung 18

## Slide 46: 다음시간 안내
[1] Electronics devices and Circuits theory – Robert Boylestad, Louis Nashelsky, Prentice Hall, 11th edition
[2] Fundamental of Microelectronics – Behzad Razavi, Wiley, Preview Edition 2006
[3] Electronics Fundamentals : Circuits, Devices, and Applications - Thomas L. Floyd, David. L. Buchla, Pearson, 8th Edition
Lesson 11: Op-Amp Applications (I)
Notes: Tài liệu tham khảo va gioi thieu bai hoc tiep theo